## Slide 1: Uv-vis spectroscopy
Presented by 3rd Nano boys

## Slide 2: Outlines
Introduction
Principle of Uv-Vis
Components of UV-Vis
Types of Uv-Vis
Applications of UV-Vis

## Slide 3: Introduction

## Slide 4: What is uv-vis spectroscopy
It is an optical characterization method that utilizes UV-Vis light to study how this light interacts with the material by measuring the absorption or transmission at different wavelengths.

## Slide 5: Principle of Uv-Vis spectroscopy

## Slide 6: Principle of uv-vis spectrSocopy
Electronic Transitions: Molecules absorb light, causing electrons to move to higher energy states:
π → π*: Double bonds (alkenes), aromatic rings (benzene).Moderate UV.
n → π*: Lone pairs (ketones, amines).
σ → σ*: Single bonds (methane).Less than 200nm
Beer-Lambert Law: Absorbance (A) is proportional to concentration (c), path length (l), and molar absorptivity (ε).𝐴=𝜖⋅𝑐⋅𝑙
Absorption Spectrum: Molecules absorb light at specific wavelengths, producing absorption peaks (λmax) related to electronic transitions.

## Slide 7: Components of uv-vis

## Slide 8: Components of uv-vis spectroscopy
Light source
Entrance slit
Dispersive element
Exit slit
Sample cell
detector

## Slide 9: Types of uv-vis

## Slide 10: Types of uv-vis spectroscopy
Single Beam Spectrophotometer : Uses a single light path; the light passes through either the sample or the blank (reference), but not both simultaneously. Simple and low-cost.
Double Beam Spectrophotometer : It splits the light beam into two paths—one passing through the sample and the other through the reference (blank)—and compares both beams simultaneously.

## Slide 12: Applications of uv-vis
Determine the concentration of a substance in a solution
Characterize chemical compounds based on their absorption spectra
Detect and measure pollutants or contaminants in the environment
Calculating band gap for electronic materials through Tauc Plot

## Slide 13: TAUC equation
Used to determine the Energy band gap of the material .
(αhν)^(1/n) =A(hν−Eg​)
α is the absorption coefficient.
h is Planck's constant
𝜈 is the frequency of the incident light.
ℎ𝜈 is the photon energy.
n is a constant that depends on the type of material (semiconductor or insulator).Transitions of the material
𝐴 is a proportionality constant
E g​ is the optical band gap energy of the material.

## Slide 14: Calculating band gap in origin